DANELY PRESS

SET UP PROCEDURES

- Turn on Main Power Switch.

- Turn on Main Airline.

- Start lube motor, (wait 15 minutes before operating press).

- Turn key to Program and bypass the Limit Switch, Tonnage Monitor, Die Protector, and turn key to run.

- Measure the height of die set and add ½”.  Ex) 13 ½” + ½” = 14” total.

- Press the Press Control Button

- Press Auto Sets.

- Press Slide Adjust.

- Turn key to Program.

- Press Change Setting.

- Punch in your shut height measurement from line 5 and Press enter.

- Turn Slide Adjust key to ON position.

- Press Auto Adjust.  (Press is now adjusting the shut height.)

NOTE:  Press has to be at top Dead center for adjusting shut height.

- When shut height adjustment is complete turn Slide Adjust switches to off and Program switch to Run.

- Start Main motor.

- Exit Slide Adjust screen.

- Exit Auto Feed setting screen.

- Turn switch key to Mode Select.

- Press Timed Inch button.

- Turn switch key from Mode Select to run position.

- Using inch control buttons jog press to bottom dead center. Hold buttons to activate timed inch. Re-press inch control buttons to jog to bottom dead center.

- Set up die set, making sure die set fits in press.

- When die set is clamped to press use inch  control buttons to set press at TDC top dead center.360(

- Turn key switch to Mode Select, press Single Stroke and return switch key to run position.

- If parts ejection is required, go back to Main screen.

- Press Limit Switch button and turn key switch to Program.

- Press Bypass button and turn key switch back to Run.

- If die protection is required Press Die Protection button.  (Right now it’s only used in Die set # GI 900-02).

- Turn switch to Program and press bypass button it should read Ok.

- Turn switch key back to Run and Exit screen back to Main Screen.

- Try your Material and if more depth is required go back to slide adjust and repeat steps 6 to 14.

- Once you have adjusted your shut height go back to Main menu.

- Press Tonnage Monitor button.

- Turn switch key to Program.

- Press Bypass button (Status should read Ok)

- With the same screen press Limits button.

- Press Auto set up button and turn switch key back too run.

- Now cycle Press/parts 16 times for auto Tonnage set up.

# A.   DIE REMOVAL

- Turn key switch to Mode select.

- Press Timed Inch.

- Turn key switch from Mode Select to Run.

- Then using the two-inch buttons to bottom Dead Center.

- Take off clamps and move back to top Dead Center.

- Turn off Power and Air supply.

- Remove Die set.