HYDRAULIC DIE SPLITTER

SAFETY & OPERATING PROCEDURES

A.	SAFETY

Never work under suspended tooling.

Make certain hydraulic table is clean.

Place or remove tooling carefully.  If it is too heavy, find help.

Assure that carts, tools, clamps, etc. are clear of hydraulic table.

Never store tools and material on motor/pump platform.

B.	OPERATION

Lock swivel top in position.

Use top spacers that are clean and parallel.

Use at least two “C” clamps to secure work piece.  For larger, heavier units, four “C” clamps must be used.

Never over-tighten, thereby weakening “C” clamps.