LIQUID PAINT BOOTH PROCEDURES

NOTE:  Both paint booth exhaust fans must be running before the compressed air will

come on.

A.	START-UP

- Lock out booth pumps.

- Scrape paint off waterfall front panels.

- Skim paint waste from each paint booth.

- Remove pump screens, scrape clean. (NOTE: that screens must be removed and cleaned one at a time to minimize paint waste transferring to pump.

- Unlock pumps.

- Start both exhaust fans for the paint booths and pressure wash.

- Start both waterfall pumps.  Ensure there is a complete curtain of water flowing. If water is not flowing proper, pump must be locked and nozzles cleaned.

- Turn on ball valves for the waterfall make-up water.

- Turn mixers on to mix the paint. -60 psi.

- Turn on all the valves for the catalyst.

- Pull on the air valve for the hydra cat. –100 to 105 psi.

- Push in the reset for the runway valve on the air motor for the hydra cat.

- Turn on the air assist for the paint guns-60 psi

- Turn on all ovens and wash.

## B.	SHUTDOWN

- Turn air on to thinner pump.40 psi max

- Flush out manifold and paint guns.

- Turn off thinner pump.

- Stop the waterfall pumps.

- Stop the exhaust fans.

- Turn the catalyst valves off.

- Shutdown wash, all ovens, lights and paint heater.

NOTE:  Leave air off to thinner pump when not in use. Damage will occur to the pump

if the air is left on.

## C.	LIQUID PAINT BOOTH MAINTENANCE

- Clean ends of guns daily.

- Clean filters daily on guns.

- Clean floor after each shift and plastic if needed.

- Scrape waterfall doors daily.

- Scrape walls of paint booths weekly or sooner if required.

# PAINTERS SHIFT CHECKLIST TRIP LINE

Date:  						Time: 				By:

1.         Start of shift - Total Track Distance:

Total Running Time:

| Daily: Start up | Initial when complete |
| --- | --- |
| Lock out paint booth pumps. |  |
| Scrape front panels of waterfall. |  |
| Skim detach from waterfalls. |  |
| Remove pump screens, one at a time, scrape and pressure wash clean. |  |
| Unlock pumps. |  |
| Start both exhaust fans for the paint booths and pressure wash. |  |
| Start both waterfall pumps. Ensure there is a complete curtain of water flowing. If water is not flowing properly, pump must be locked and nozzles cleaned. |  |
| Turn on ball valves for the waterfall make-up water. |  |
| Turn mixers on to mix the paint. -60 psi. |  |
| Turn on all the valves for the catalyst. |  |
| Pull on the air valve for the hydra cat. –100 to 105 psi. |  |
| Push in the reset for the runway valve on the air motor for the hydra cat. |  |
| Turn on the air assist for the paint guns-60 psi. |  |
| Clean gun filters, air caps, gun nose, outside gun threads, check guns before placing back on guns. |  |
| Inspect Dry-Off Oven, Bake Oven, and Wash for parts which may have fallen off and/or other safety/quality concerns |  |
| Check ground cables and ensure they are all in place. |  |
| Check and ensure dip tank ground cables are in place. |  |
| Check paint catalyst & thinner levels. Get more if needed. |  |
| Check viscosity on dip tank and adjust. |  |

| End of the Day: | Initial when complete |
| --- | --- |
| Flush out guns. |  |
| Pick up plastic bags, plugs, and caps from booth floor. |  |
| Change dirty light bags. |  |
| Change dirty gun covers. |  |
| Check and clean (if necessary) filter screens in waterfalls. |  |

* Note:	White rag test to be done on first pretreated parts of the day-day shift only.  Hand rags in with this sheet.

- Oven Temperatures	Time:

| Oven Temperature ◦C |  |  | Comments: |
| --- | --- | --- | --- |
| Dry Off Temp ◦C |  |  |  |

- General notes and comments regarding housekeeping and maintenance.