MANUAL LATHE PROCEDURE

A.	SAFETY

# Wear personal protective equipment.

# Use a face shield where flying chips are present or a chuck shield if equipped		  with one.

# Wear rubber gloves when working with coolant.

# Remove the chuck wrench immediately after adjusting the chuck.

# Make sure the forward/ reverse lever is fully disengaged before using the chuck wrench.

# Always let the chuck come to a complete stop before touching the part or the chuck.

# If in some instances flying chips are unavoidable, please use a curtain to prevent other operators from being subjected to burns, etc.

# Be very careful while filing, emerying and when using a deburring tool.

- Do not operate the lathe wearing loose clothing, finger rings or other jewelry. Long hair must be tied up or tucked under the hard-hat.

- Never attempt to remove chips by hand, turn off the lathe and use a chip hook or a brush.

- Never polish a part with emery cloth wrapped around your hand, hold the emery cloth using your thumb and forefinger only.

- When emerying a threaded part use a course grit sandpaper to minimize the surface to surface contact, which will reduce the tendency for the emery cloth to want to grab.

- When changing or inverting secondary jaws

- Inspect the condition of the bolts- if they are not in good condition they must be replaced.

- Inspect internal and external threads

- Inspect all mating surfaces for wear burrs etc.

- When re-installing the secondary jaws (soft jaws) you must torque the cap screws.

The following are recommended torque specs for 3/8”; 1/2” alloy cap screws.

3/8”x 24TPI, max 50 ft/lbs.

½” x20TPI, max 120 ft/lbs.

B.	OPERATING

# Ensure the main power is turned off when doing Total Preventive Maintenance.

# Know where the emergency stop button is located on your machine before operating.

# Practice good house keeping, return tools to the proper location after use.

# Try to eliminate long, stringy chips when machining as they can be easily caught up in the chuck and cause personal injury, always exercise proper chip control.

# Know machine speeds and feeds, if you are unsure please ask your supervisor.

# Make sure cutting tools are used properly and for their intended application.

# Do not try and fix the machine if there is a problem, ask your supervisor to contact plant maintenance.

# Ensure that auto stops are set before starting a job.  Make sure cutting tools are centered and securely fastened.

- Ensure the lathe you operate and tooling is used with respect at all times.

- Never use compressed air to clean the lathe, as small particles may become embedded into parts of the machine causing damage, use a soft bristle brush.

- Never leave a running (spindle turning) lathe unattended.