HECKERT MILL

SAFETY & OPERATING PROCEDURE

SAFETY:

- Do not set up or operate the Heckert Mill unless you have been properly trained by your Production Supervisor or Universalist.

- Do demonstrate proper safety (operating awareness at all times).

- Do not remove drill chips by hand, use provided chip hook.

OPERATION:

- Do ensure that the required mill jig is used and securely fastened.

- Do ensure proper cutting tool is used, securely fastened and rotating in the proper “Forward” cutting direction.  (Inspect all cutters for wear, nicks, sharpness, and hairline cracks before actual set-up).

- Do ensure that proper speed (RPM) and feed (inches - per minute) is used.  According to the type of material being used, and diameter of cutting tool.

- Do ensure that all stopper dogs are used, set up in proper sequence and fine-tuned for specific job.

- Do a dry run, “without work piece”, to ensure that spindle is turning in proper direction, stopper dogs are set and functioning properly and coolant flow is adequate.

- Do ensure there are no objects restricting the travel of the mill table.

- Do ensure that the hydraulic clamping on the sub-plate is sufficient to securely fasten work piece.

- Do ensure that when using A Hougen cutter, the slug is removed after each cycle.

- Do not use the red emergency STOP button as a regular stop button.  This will result in internal gear damage.

- Do ensure that before mill is cycled all tools or miscellaneous items are removed from the mill table.  Failure to do so could result in personal injury, tooling/machine damage.

- If a slug gets stuck in the Hougen cutter, tap the outside of the cutter lightly with a rubber hammer.

- If at any time the machine has to be STOPPED during the “cycle”, the table must be returned to the home position “Fast Down” to prevent machine / tooling damage.