PALLET LIFTER

SAFETY AND OPERATING PROCEDURES

Do's:

Wear personal protective equipment.

Two people must operate this lifting device.

The lifter may only be used for its intended purposes:

a)		For the weighing of banded 11 gauge salvage;

b)	For the transfer of materials from the rear of the shear to the operator's side that are on pallets, open-ended jig stands, or baskets ONLY!

The operator shall visually inspect the lifter before using it.

The operator shall watch carefully that the lifter is performing properly during lifting and transporting.  Travel smoothly and make no sudden stops.

The fork pins must be in place whenever the lifter is being used.

Do a trial lift of 8" to 12" to ensure that the load is level and secure.

Make sure the crane link is in a notch before lifting.

Don'ts:

Do not lift loads beyond the rated capacity of the pallet lifter.

The lifter shall not be raised above a height of 48".  No exceptions.

Do not lift long loads more than 6" high that may fall over.

Pallets of sheared strips must not be lifted onto shear table with the pallet lifter.

Do not attempt to stack baskets under any circumstances.  No exceptions.

Do not attempt to move sheets of any gauge.