#8353 QUALITY CHECK PROCEDURE

(WS PANEL MOUNT BRACKET)

Note:  Due to the large number of pieces breaking, we require a procedure to set a standard on how to check the quality of each piece. The breakage may be a result of an improper design, a manufacturing default or a combination of both.  Therefore, the following testing must be done until the problem has been corrected!

Check each piece before it is used in a bag, assembly, or crate

Give the piece a diagonal twist to see if it will break at the corners.

Hold the bracket with one hand on each end of the bracket, and at the corners of the cross pieces. Place your index fingers at diagonal corners at the back of the piece with your thumbs on the opposite diagonal corners at the front of the piece.

Apply moderate pressure to twist the piece. The piece should be twisted about ¼” from its natural state. Continue the pressure for about 2-3 seconds.

Change positions of your thumbs and of your index fingers and give the piece a twist in the opposite direction. Continue the pressure for 2-3 seconds.

If the piece did not break it is, then it is OK to use. If the piece broke or cracked at the corners, then it failed and must be rejected.

Place the rejected parts in a container, write up a non-conformance form and a reject form and take the rejected parts to the material management ‘return’ department.