SAFETY

LIMITS - WEIGHT AND SIZES

- Conveyor Limits

  - From The bottom link to the floor is 12 ft. 6 ¼”.

  - Parts must be within the following limits:

    - Minimum 15” off the floor.

    - No more than 24” from the center of the track.  Except for the NW-626 and NW-627 wings for the NW-626 bundle.

  - 500 lbs. per carrier roller.

Use Load Bars if weight exceeds 500 lbs. /carrier.

- Hook Limits

  - No hooks can go through the wheelabrator empty.

  - When the bottom of the hook runs parallel to the line it must be a single unit (one hook) and must hang a minimum of 30” below the bottom link.  Exception:  A 24” hook can be used hanging off bottom link, only when used in conjunction with a tillage paint load bar.

  - Whenever the hook that hangs directly off the conveyor bears any weight, the top of the hook should sit, whenever possible, so that the chain link remains in its natural position.  If it is not in its most natural position, there is a tendency to bind around corners.  The most natural positions of the chain links are as follows:

- Bottom Link - top of hook parallel to line.

- 2nd Link - Top of hook perpendicular to line.

- 3rd Link - Top of hook parallel to line.

  - 30” hook

- Can hang off the 3rd link only when used in conjunction with a paint load bar.

- Can hang off the bottom link on larger weldments.  Bottom of hook can be parallel or perpendicular to the line.

- When hanging shank racks off 30” hooks, both the 30” and the shank rack hooks must be parallel (in line) with the paint rack.  The 30” hook in the bottom or 3rd link in this case.  The shank rack hook must face forward.

- Note:  When hanging a shank rack from 30” hooks, the tie down hanger cannot be hung over the shank rack but rather must be hung from the shank rack hooks.

  - 40” hook

- Can hang off of any link (except the top one) and can run parallel or perpendicular to the line.

Caution:  Hooks with On/Off or Paint/No Paint welded on them cannot be hung directly off the paint track.  The signs will not fit through the top of 	the wheelabrator.

- Guidelines for Parts

  - Maximum length is 36 ft. long at 2 ft. wide and 30 ft. long at 4 ft. wide.

  - Maximum height is 8 ft 9 inch.

  - Maximum width is 4 ft.

  - Items should be spaced equally beyond support points.

  - Maximum distance between supporting points is 12 ft.

“Supporting Points” refer to the outermost chain on the conveyor that bears any weight from that part.

- Hook Ratings

  - Shank Racks

¼” - 75 lbs. per hook

3/8” - 139 lbs. per hook

Total - 700 lbs. per rack.

  - Hooks

| Round Bar |  |  |  | Square Bar |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Size | Style | Capacity lbs | Date Tested |  | Size | Style | Capacity lbs | Date Tested |
| 1/4" | 4" S | 58 | 2/14/02 |  | 1/2" | 8" S | 375 | 2/14/02 |
| 1/4" | 8" S | 62 | 2/14/02 |  | 1/2" | 16" S | 362 | 2/14/02 |
| 1/4" | 8" B | 55 | 2/14/02 |  | 1/2" | 30" S | 340 | 2/14/02 |
| 3/8" | 16" S | 124 | 2/14/02 |  | 1/2" | 40" S | 416 | 2/14/02 |
| 1/2" | 8" S | 330 | 2/14/02 |  | 1/2" | 8" B | 375 | 2/14/02 |
| 1/2" | 16" S | 320 | 2/14/02 |  | 1/2" | 16" B | 445 | 2/14/02 |
| 1/2" | 8" B | 280 | 2/14/02 |  | 1/2" | 24" B | 450 | 2/14/02 |
| 5/8" | 8" S | 630 | 2/14/02 |  | 1/2" | 32" B | 400 | 2/14/02 |
| 5/8" | 16" S | 575 | 2/14/02 |  | 1/2" | 40" B | 360 | 2/14/02 |
| 5/8" | 24" S | 525 | 2/14/02 |  |  |  |  |  |
| 5/8" | 30" S | 535 | 2/14/02 |  |  |  |  |  |
| 5/8" | 40" S | 525 | 2/14/02 |  |  |  |  |  |
| 5/8" | 8" B | 592 | 2/14/02 |  |  |  |  |  |
| 5/8" | 16" B | 550 | 2/14/02 |  |  |  |  |  |
| 3/4" | 12" S | 1000 | 2/14/02 |  |  |  |  |  |
| 3/4" | 16" S | 1030 | 2/14/02 |  |  |  |  |  |
| 3/4" | 30" S | 1035 | 2/14/02 |  |  |  |  |  |
| 3/4" | 8" B | 1030 | 2/14/02 |  |  |  |  |  |
| 3/4" | 10" B | 1015 | 2/14/02 |  |  |  |  |  |