TANK PAINT LINE

OVEN CLEANING PROCEDURE

Oven Cleaning Process

Warning:  All ovens must be kept clean.  Failure to remove the dust and dirt will result in paint finish contamination and more importantly a fire hazard.

- CURE OVEN

  - Following Maintenance Lockout Procedures.

  - Remove any plugs and debris.

  - Sweep down oven in following sequence:

    - Blow of I - Beam, Scotch Brite or grind off if needed.

    - Ceiling

    - Duct Work (inside and out).  Use access doors cut in duct to avoid changing baffles on duct work.

    - Walls and support beams.

  - Inspect oven and if powder is building up grind off build up.

Note:  Make sure when grinding not to gouge the walls.

  - Vacuum out floor inside duct work.

  - Sweep floor in oven.

  - Mop walls and floor.

  - Blow off any affected parts.

  - Sweep off top of oven.

  - Inspect burner box and vacuum out as needed.

- DRY OFF OVEN

  - Blow off I - Beam, Scotch Brite or grind if needed.

  - Sweep down walls.

  - Sweep floor.

  - Mop walls and floor.

  - Sweep off top of oven.

  - Clean any dust that fell from the top of the oven when sweeping.

  - Inspect burner box and vacuum.

- PREPARE FOR USE

a)	Remove all tools, vacuums, cords, lights etc.

b)	Remove all locks.

c)	Run fans and exhaust fan to remove any dust.