WASH CLEANING PROCEDURE

Note:  This procedure should apply to washes.

Safety:  Follow all lockout procedures prior to entering the wash.  Entire panel can be shutdown.  Make sure individual pumps are locked out if burners need to be fired before you are done working inside the wash.

The Following is to be done, and Daily Schedule/Check sheet filled out:

- a)	Remove all risers from each stage being cleaned, including misting risers			between stages.

b)	Remove nozzles and end caps from risers.  Keep each stage separate.

- Mix a 10:1 solution of Oakite 32 (10 parts water to 2 parts Oakite 32) water first then Oakite 32.

- Soak and agitate (with air wand) tips in solution until clean (nozzles may need to be disassembled periodically when they start to get sludge built up).

- Dump Oakite and water mixture and rinse nozzles in fresh water until clean.

- Transport risers to manual wash bay. Always drive the forklift in reverse in order to minimize the chance of damaging the risers.

- Pressure wash risers inside and out.  Also visually inspecting nozzles for cracks or breaks.  Notify FLS if any risers require repair.

- a)	Scrape down walls in each stage to remove any sludge or scale that may be		building up.  Wash off any remaining sludge.

- Remove screens from each stage and wash.

- Drain one rinse stage weekly, pressure wash out the inside and refill with fresh water.  (Except SPL rinse.)

- Replace screens in each stage.

- Checks to make sure all drains are closed and fill valves are shut off.

a)	Re-install nozzles on risers.

- Re-install risers in wash.

- Re-align nozzles.

- Turn pumps on to flush any loose sludge out of the risers.

- Re-install end caps on the risers.

- Check again for plugged nozzles, clean and replace.

- a)	Remove anything from wash that does not belong.  (EX:  Lights, scrapers, etc.).

b)	Final inspection, check that the Banjo clips are done and the end caps are all		one.

- Close all access doors and remove all locks.

- a)	Sweep off the top of the wash.

b)	If dust is swept off the edge, make sure areas below are also swept up.

- Make sure areas worked in are left in as good, if not better shape then when you came.

# Text boxes

Warning:  Be sure all personal protective equipment is worn and the directions on the supplier label are followed.