5 - STAGE WASH

OPERATING PROCEDURE

Note:  Wash should be started at 6:45 a.m. at the latest, or 1 hour before the shift begins.

A.	SYESTEM START UP

- Turn on the main power control (breaker switch) located on the right side door panel of the cabinet (after weekends & lockouts).

- Check the low level water lights if any are lit the level is that particular stage is too low and water will have to be added to get the level up and then the light will go out.

- Washer fans start up.

  - Turn the main power control (breaker) switch this should only be turned off for weekends or lockouts.

  - Turn the switch to auto, the lights will not light up or start until the temperature in the wash cabinet reaches 33(C and fans will shut off automatically when the temperature is below 33(C.  This is done so we can exhaust the heat and steam so the track I beam will not rust.

- Do not start the circulating pump and leave on until the wash stages are up to temperature.  If they are started when the wash stages are cold the tanks will foam over.  The pumps should be started and ran for 2 minutes and then turned off.  This will mix the hot and cold water together this way the entire stage heats up.  This should be done periodically.

B.	WASHER FOR HEATED STAGES (STAGE WITH BURNERS)

- Push in the combustion blower button.

  - Combustion blower light comes on.

  - Combustion blower starts.

Note:  The wash pumps can be started without the combustion blower being on.  However, the combustion blower must be on for the wash burner circuits to operate.

  - There is a 90 second time delay from combustion blower start until the pilot light comes on.

  - The pilot light timer starts and the pilot light comes on.  The main flame will start and the white light will come on when the pilot timer is complete.

- Turn the alarm switch to on.  The alarm will go off if there is an ignition failure, low water level or if a circulating pump stops.

C.	SYSTEM SHUTDOWN

- The 5-Stage Wash can be shutdown 2 ways.

  - Push the emergency stop button.  All lights will go out and everything will stop.

  - Push the individual stop button for each function for each stage.

If you are pushing each stop button the alarm must be turned off first.

The individual stop button will only shut off the function for the button you push.  (i.e.:  If you stop stage 1 blower off stage 2 will still be operating.)

- Turn off the main power control (breaker) switch for weekend shutdown or for lockout only.  The switch is expensive to replace and there is no need to turn the breaker off over night.

D.	WASH PUMPS ONLY

You may want to stop the circulating pumps but still have the blowers operating.  This will allow you to maintain the desired temperature of the wash tanks and not operating the circulating pumps.

E.	WASH BURNERS

To turn off the combustion blower push the stop button for the blower for the stage you want turned off.  All the lights for that stage will go out and the blower, pilot and main flame will stop operating.