BLAST MACHINE

ABRASIVE DRUM HANDLING

PROCEDURES

Safety:	Never stand or walk beneath the raised mast of a forklift, and always stay clear of the fall zone.

Adding Abrasive in a Drum with a Lid

- Select the proper drum of abrasive.

- Ensure that the lid is securely attached.

- Contact a forklift driver to assist you.

- The forklift driver will attach the drum handler to his/her forks.

- Attach the drum handler to the drum.  Ensure all connections are secure so that the drum will not slip or fall.

- The forklift driver will raise the drum above the abrasive adder hopper.  Guide the forklift driver until the drum is centered above the spike on top of the hopper (stay clear of the fall zone).

- When the drum is centered, the forklift driver will then lower the drum piercing the drum bottom.

- When the drum is resting on top of the hopper, use the ladder provided to disconnect chain holding the drum in the handler.  Be sure to be clear of the fall zone before the forklift driver has pulled away from the drum.

- Sweep up any spilled abrasive.

Removing an Empty Drum

- Contact a forklift driver to assist you.

- Attach the drum handler to the forks.

Note:  Never remove an empty drum by squeezing together the forks around the barrel.  Always use the drum handler.

- Raise the handler to the proper height and attach the handler to the drum.  Ensure all connections are secure so that the drum will not slip or fall.

- Raise the drum above the hopper.  Allow any abrasive to drain out of the hole in the bottom.

- Lower the drum and remove the lid.

- Raise the drum above the hopper again and rotate the drum upside down, emptying out the drum completely.

- When the drum is empty, lower it and remove it from the handler.

- Sweep up any spilled abrasive.