550 CASTING PNEUMATIC DRILL/TAP

SAFETY & OPERATING PROCEDURES

Due to the nature of this operation machine damage, tooling damage and personal injury can occur, which mandates the following procedures must be applied.

SAFETY:

- Air lines must be disconnected before attempting to change or adjust the drill and tap in order to prevent personal injury.

- Inspect the condition of the air lines and fittings.

- Inspect for cuts and wear.

- Inspect fittings for leaks.

OPERATION:

- Operating controls.

- Test the pneumatic drill for proper spindle rotation, feed and feed return.

- Inspect the return spring and swivel on the pneumatic tap.

- Do not adjust the feed/feed return on the pneumatic drill before consulting with your Supervisor.

- Casting stoppers.

- Flip Down Stoppers:  Select proper stopper for the casting being drilled.  Refer to the engineered drawing for specifications.

- Ensure the casting rests against the correct lower stopper.  Stoppers are		    labeled.

- Verifying the correct tooling.

- Inspect the condition of the drill bit - chipped edges and evidence of extreme heat are not acceptable.  The cutting edges should be sharp.

Bit Type:  7/32” HSS Straight Shank.

- Inspect the condition of the tap being used.  Tap should be sharp with no chipped or worn edges.

Tap Type:  1/4”, 28 UNF, Blue Hybrid ground thread spiral point tap (available from warehouse).

- Ensure lubrication reservoir has at least 50% capacity.

Lubrication Type:  Rapid Tap - Review WHMIS sheet for Rapid Tap.

- Install casting, drill hole.

- Slide casting onto top casting guide against stopper.

- Press drill start button.

- Inspect hole when drill completes cycle. (Check diameter with a caliper).

- Adjust drill depth if necessary.

Tap hole.

- Slide casting on casting guide.

- Lubricate tap - submerse tap in rapid tap lubricant (do this for each hole	 tapped).

- Align tap to hole.

- Tap hole - a minimum of 4 threads must be present, 7 threads maximum.

- Inspect thread - check thread with 1/4” grease nipple - fit should be snug.

QUALITY

- It is the responsibility of the operator to produce quality parts.  Check your parts frequently, every 5-10 pcs.

- Communicate any problems to your Supervisor.

PRODUCTIVITY

- Practice good housekeeping at all times.

- Put tools in proper place when not in use.

- Ensure immediate area and floor space is clutter free.

- Ensure drill, tap are inspected regularly.