CHAMFERING MACHINE

SAFETY & OPERATING PROCEDURES

- Before proceeding with any set-up or operation you must be fully capable of understanding and applying the content of this procedure.

- Never operate the chamfering machine unless you have been formally trained by your F.L.S. or designate.

A.  SAFETY

- Make sure all personal protective equipment is worn when setting up or operating the chamfering machine.

- Inspect debris shrouds to ensure they work properly and are always used during operation.

- Never ram the cutters against the work piece with cutters rotating or idle.

- Never put your hands near a rotating cutter.

B.	PRE-OPERATION

- Before operation inspect the condition of the cutter.

- If it is worn chipped or broken either rotate, invert or replace the cutter (insert) with a Kennametal SNMP-643 KC-850 insert.

- When rotating, inverting or replacing your insert.

- Inspect the condition of your clamping screw and insert seat for wear.  Replace if necessary.

- Inspect the condition of the machine including:

- Safety Devices

- Chuck Jaws

- Bed, Guides

C.	OPERATION

- With a rag, clean the clamping surface on the part being chamfered.  (Make sure chuck jaws are clean).

- When inserting your part make sure the cutting head is retracted.

- Insert your part into the chuck; make sure it is against the stopper.

- Snugly tighten your part with the chuck wrench (or air chuck if applicable).

- Start the spindle.

- Manually feed the cutter up to your work piece.  As soon as the cutter makes contact with the material shut off the spindle.

Note:  This only has to be done for your set-up piece.

- Measure the distance between the table stopper and the bed.

- The distance between the stopper and the bed should be the same as the length of chamfer.

E.g.:  Distance between stopper and bed ¼”

Required Chamfer ¼” x 30o

- If the stopper distance is what is required on the drawing move the cutter away from the work piece and re-start the spindle.

- Hand feed the cutter towards the work piece until the feed handle stops turning.

- Return the spindle to the start position.

- Shut off the spindle rotation.

- Unclamp and remove the work piece (either manually or with the use of the air chuck).

- Complete remaining parts.