## DISK / BELT SANDERS

# A.	SAFETY

1.   a)	Gloves are recommended to be worn when grinding parts larger than 4” x 4”.

- Gloves are not recommended when grinding parts smaller than 4” x 4”used in conjunction with a parts rest) or when sharpening drill bits.

- For the purpose of inspection or adjustment or anytime the safety cover is opened deems locking out the power supply on the machine.

- Eye protection such as a face shield must be worn.

B.	DISK / BELT INSPECTION

- Release the latch on the safety cover.

- Open door exposing drive components.

- By hand rotate the disk/belt one full revolution.

- Inspect for cuts, nicks and excessive wear.

- If sanding disk/belt is deemed useable, proceed with operation, if unusable		replace the belt.

# C.	REPLACING THE SANDING BELT

After the belt has been replaced, check belt tension/tracking.  Monitor belt tension/tracking after the belt has been changed

D.	REPLACING THE SANDING DISC

After the old sanding disk has been removed, clean all adhesive residues off the machine platen.

E.	GENERAL OPERATION:

- Material rest should be adjusted to a minimum 1/32”, maximum 1/16” clearance.

- Should handling smaller parts put you or people around you at risk, use alternate holding methods.

  - Pliers.

  - Vice Grips

F.	OPERATION

- Ensure belt sander (inside/outside) is kept clean at all times.

- Ensure floor and surrounding work area are clutter free.

- Ensure tools are cleaned and returned to their proper place after use.

- Use moderate pressure when belt sanding.

- Use full width of belt to ensure belt wears evenly.

- Material under 3/16” must be held flat on material rest to avoid the part from being wedged between the belt and the material rest.

- Hand held scrapers are not to be sharpened on the belt sander, use a pedestal grinder.

- Use common sense at all times, if something does not seem right contact you’re FLS.

EXCEPTION: TO GRIND SMALL PARTS ABOVE THE PARTS REST WHILE WEARING GLOVES (ONLY APPLICABLE TO THE VERTICAL BELT SANDER)

a)	Grinding small parts, ensuring the part is fed into the belt at an angle

b) 	Thin material can also be de-burred using this method.

  - Never grind small parts on the parts rest without holding them securely with pliers, vice grips etc. Even when parts are big enough not to get wedged between the parts rest you should still secure them as they can wobble and damage the belt.]

  - When using the sanding disc always work on downward side of rotating platen/disc.