FLOOR SWEEPER PROCEDURE

(Power Boss Sweeper, Unit #127)

- OPERATOR RESPONSIBILITIES

- The floor sweeper should never be operated unless the operator has been fully trained in this procedure and has been given practical instructions from a competent person.

- The floor sweeper should never be operated unless the machine has been inspected and found to be free from malfunctions and potential safety hazards.

- The operator must complete a TPM checklist before operating the floor sweeper at the beginning of each ‘Day’ shift, and post the sheet on the machine.

- The operator must always demonstrate respect for personal safety, the safety of others, and respect for property while operating the floor sweeper.

- BEFORE STARTING THE ENGINE

- Before starting the engine, make sure that:

- a complete TPM check has been performed at the beginning of the “Day” shift and the TPM checklist completed.

- you check the brushes and brush skirts for damage, wear, and adjustment.

- you are securely seated in the operator’s seat.

- the parking brake is locked.

- the directional control petal is in neutral.

- the throttle is in the idle setting.

- the hydraulic controls are in “OFF” position.

- FLOOR SWEEPER OPERATION CHECKLIST

This inspection should be done with the engine started but before you begin your duties.

- Sound horn

- Check headlights and warning lights

- Check steering wheel for excessive play

- Listen for any abnormal noises

- Check panel gauges and lights

- Check brakes - petal smooth, functions well, emergency brake holds.

- Lift and tilt hopper - run vibrator

- Shifting - shifts into forward, reverse, neutral smoothly

- DURING OPERATION

- Always operate the machine at a safe speed for the conditions.  Slow down, sound horn, and yield to pedestrians.  Operate at slower speeds in tight areas and near machinery and other equipment.

- Keep your hands and feet within the cab area.

- Use the safety hazard lights when sweeper is in motion.

- Do not sweep oversize debris, (i.e.:  welding wire, string, cardboard, etc.).  This remains the responsibility of the people who sweep stuff into the aisle.

- Try to arrange your sweeping pattern using long runs to avoid starting, stopping, and excessive cornering.  Try to avoid sudden turns if possible.

- Travel slowly on grades and avoid parking on inclines.

- Never operate the sweeper outside off the concrete pads.

- Do not run the vacuum or the brushes in wet or snowy conditions.

- Do not drive with the hopper in the raised position except the few feet necessary to position the hopper over the dumpster when dumping.

- Be alert at all times.

- When leaving the sweeper:

- Place the controls in “OFF” position

- Set the parking brake

- Bring the engine to an idle, and let it idle for about 30 seconds

- Shut off the engine

- When necessary, operate the shaker to clean the filters, - run the vibrator through a minimum of 3 cycles.

- CLEANING AND MAINTENANCE

- Always stop the engine and set the parking brake before servicing.

- Always engage the “Safety Arm” before getting under the hopper.  Do not rely on the hydraulic cylinder to keep the hopper raised.

- Follow the “Propane Tank Changing and Handling” Procedure FCS010 when changing propane tanks.

- Inspection and clean the brushes as follows:

- Engage emergency brake

- Raise the hopper

- Engage safety stop arm.

- Shut off engine.

- Open inspection covers.

- Inspect and clean brushes, removing accumulated debris

- When inspection and cleaning is complete, reverse the above steps to return sweeper to normal operating condition.

- To empty the hopper follow the following steps:

- Drive and align sweeper to the dumpster - make sure that the sweeper is on a level surface.

- Raise hopper to the dump position.

- Drive forward to position hopper over dumpster.

- Tilt the hopper to empty it.

- Run the vibrator during the dumping procedure.

- Reverse the above steps after the dumping operation is complete.

TPM CHECKLIST FOR POWER BOSS SWEEPER

PERFORM VISUAL INSPECTION OF SWEEPER

FOR WEEK OF 				TO

| VISUAL INSPECTION CHECKLIST | SIGNED: |  |
| --- | --- | --- |

|  | (specify time of inspection) | AM | PM | AM | PM | AM | PM | AM | PM | AM | PM | AM | PM |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | (some points within this checklist may not be | MON | TUE | WED | THU | FRI | SAT |
|  | applicable, use your discretion) |  |  |  |  |  |  |
| 1 | Check hour meter reading. If needed have your supervisor make arrangements for servicing. |  |  |  |  |  |  |  |  |  |  |  |  |
| 2 | Cab clean - no garbage, empty cans, scrap banding bins empty, no loose tools lying around. |  |  |  |  |  |  |  |  |  |  |  |  |
| 3 | Battery - cables and battery mounts secure. |  |  |  |  |  |  |  |  |  |  |  |  |
| 4 | Engine oil level - add if necessary. |  |  |  |  |  |  |  |  |  |  |  |  |
| 5 | Radiator - water level okay. |  |  |  |  |  |  |  |  |  |  |  |  |
| 6 | Inspect and Adjust Brushes |  |  |  |  |  |  |  |  |  |  |  |  |
| 7 | Evidence of damage - on any part of the sweeper - collision etc. |  |  |  |  |  |  |  |  |  |  |  |  |
| 8 | Tires - visually inspect for adequate inflation, nicks & cuts. |  |  |  |  |  |  |  |  |  |  |  |  |
| 9 | Fuel - oil leaks on ground or on sweeper. Check fittings. |  |  |  |  |  |  |  |  |  |  |  |  |
| 10 | No loose bolts, parts, tools, chains left loose on sweeper |  |  |  |  |  |  |  |  |  |  |  |  |
| 11 | All guards, chains and hoses in place. |  |  |  |  |  |  |  |  |  |  |  |  |
| 12 | Hoses - not loose or worn due to rubbing. |  |  |  |  |  |  |  |  |  |  |  |  |
| 13 | Fire extinguisher - charged and functional. |  |  |  |  |  |  |  |  |  |  |  |  |
| 14 | Check operation of sweeper - horn, brakes, gauges, listen for abnormal sounds |  |  |  |  |  |  |  |  |  |  |  |  |

NEXT SERVICE DUE:

NOTE: If any item from this inspection does not check out, do not use the sweeper before contacting your immediate supervisor.

COMMENTS: