LOADING

HOIST #309, #310, #356, & #357

INSPECTION PROCEDURE

This inspection is to be done at the beginning of every shift.

Each department is responsible for ensuring that the hoists in their area are checked.

Rigging, straps and other such lifting aids are not included in this procedure.  They are the responsibility of the individual using them to ensure that they are safe to use.

In order for a hoist to be in use, it must pass all of the following inspections.

- Ensure the operating mechanisms and controls function properly.

- Safety shut-off switch.

- All directional controls.  (Some hoists have   multi-speeds).

- Horn (if equipped with one).

- Limit switches up/down.

- Inspect the control cable/chain and housing for:

- Any cracks or cracking in cable or chain.

- Any cracked or missing control covers etc.

- Any stress or broken connection on electrical wiring.

- Inspect hook and load block for:

- Deformation

- Any cracks

- Inspect safety latch for:

- Proper closure

- Spring is secure and working properly.

- Latch is in good condition and working properly.

- Inspect hoist chain/cable:

- Visual wear i.e.: Fraying

- Elongation

- Any twisting of chain links.

- Wear

- End truck drives and trolley operation.  Operate hoist in all directions and inspect for:

- Drives operating freely.

- Twisting

- Unusual noises

- Free gliding of non-powered directions.

- Inspect travel brake when operating with no load at full speed.  The 3-5 Ton Hoist should come to a complete stop in 4' to 5' feet.  The 1/2 - 3 Ton Hoists should stop in 2' - 3’ feet under the same conditions.

Note:  Vertical brakes are inspected by Plant Services.  If it becomes evident during operation that the brakes are not holding lock-out the hoist for repair and fill out a Work Order for Plant Services.

- Photo eye.  In work areas where two or more hoists are on the same track check the Photo eye by moving each of the hoists (one at a time) in the direction of the other.  The Photo eye should shut the hoist off when any two of the #309, #310, #356, and #357 hoists come within 15 ft each other. (30 ft distance is common with 5 Ton Hoists, and the smaller hoists located in such places as weld stalls are generally set up with a range of 2 feet).

Note:  Step 9 pertains to the loading hoist 309, 310, 356, & 357 in the Plant Paint Line loading area ONLY!!

9.  To test the limit switch for the trolley pull the lifting chain and load block all the way	to the east.  The trolley should be directly above the paint track.  With the load		block in your hand run the hoist to another stall.  The hoist should only be functional	with the trolley directly above the paint track and as far to the east as possible.

Failure to pass any of the above inspections must result in the immediate lock-out (follow Plant Lock-Out Procedure) of the hoist and the Department Supervisor notified immediately.  The hoist must remain locked-out until all appropriate corrective action has been taken and hoist rechecked to ensure proper operation.

Note:  Inspection of all slings, straps and lifting devices are the responsibility of each individual operator as per Standard Sling Procedure.

If their is a problem with the hoist a Work Order should be directed to Maintenance Department. The checklist that the problem was first detected on should be kept on file for reference purposes.  Until the problem is corrected.

If there are no problems during the weekly checks the checklist may be thrown away at the week’s end.

HOIST INSPECTION FOR HOISTS #309,#310,#356,& #357 CHAIN, CABLE HOISTS

At the beginning of each shift the following checks should be made by the hoist operator or designate.  If anything does not check out, lock out the hoist using proper LOCKOUT PROCEDURES.  Do not operate the hoist before contacting your immediate Supervisor.

| Week Date: |  |  | Area: |  |  | Hoist #: |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

Refers to (Company) Hoist Safety Inspection for explanation and procedure.

|  | MONDAY | TUESDAY | WEDNESDAY | THURSDAY | FRIDAY | SATURDAY |
| --- | --- | --- | --- | --- | --- | --- |
| ITEMS | A | B | C | A | B | C | A | B | C | A | B | C | A | B | C | A | B | C |
| Ensure the operating mechanisms and controls function properly |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Inspect the control cable/chain and housing for cracks etc. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Inspect Load Block and hook for cracks & deformation. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Inspect Safety Latch (Throat Latch) for proper function. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Inspect Hoist Chain/Cable for visual wear, elongation, twisted links and fraying. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Inspect end Truck Drives and Trolley operation. Operate hoist in all directions and inspect for drives operating freely, twisting, unusual noises, free gliding of non-powered direction. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Inspect brake operation. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Inspect function of the photo-eye. The #309, #310, #356, and#357 hoists should not come closer than 15 ft. of each other, (30’ for 3 - 5 ton hoists and generally 2 feet on other smaller hoists equipped with photo-eyes). |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Safety limit switches. Does the hoist stop before running into the I beam. Does the hoist move from stall to stall when the hoist is all the way to the east contacting the limit switch. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Checked by (Initial and employee number): |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |