LATHE FEED TUBE

SAFETY AND OPERATING PROCEDURES

INSPECTION

1.	Prior to set up or operation the feed tube must be checked for level and alignment.

OPERATION

1.	Under normal operating circumstances the material will be inserted into the feed tube from the far end.  The material will be advanced by using the Bar Puller.

2.	Less than full lengths of material may require the material to be fed from the operators end.  In which case the feed tube will be unclamped and off-set so that the material may be inserted into the feed tube.

3.	Regardless which method is used it is critical that to avoid machine damage and potential personal injury the feed tube must be returned to the safe operating position, and securely clamped.