NORTH PAINT LINE

OVEN CLEANING PROCEDURE

Oven Cleaning Process

Warning:  All ovens must be kept clean.  Failure to remove the dust and dirt will result in paint finish contamination and more importantly a fire hazard.

- CURE OVEN

  - Following Maintenance Lockout Procedures.

  - Remove any plugs and debris.

  - Sweep down oven in following sequence:

    - Ceiling

    - Duct Work (inside and out).  Use access doors cut in duct to avoid changing baffles on duct work.

    - Walls and support beams.

    - Front and backs of infra reds.

  - Vacuum out floor inside duct work.

  - Sweep floor in oven.

  - Mop walls and floor and duct work.

  - Blow off any affected parts.

  - Sweep off top of oven.

  - Inspect burner box and vacuum out as needed.

- DRY OFF OVEN

  - Blow off I- Beam, Scotch Brite or grind if needed.

  - Sweep down walls.

  - Sweep floor.

  - Mop walls and floor

  - Sweep off top of oven.

  - Clean any dust that fell from the top of the oven when sweeping.

  - Inspect burner box and vacuum out as needed.

C.	PREPARE FOR USE

a) Remove all tools, vacuums, cords, lights etc.

b) Remove all locks.

c) Run fans and exhaust fan to remove any dust.

D.	MEZZANINE

- Blow off top of cooling, track drive and shelving.

- Sweep up dust on floor.