# PIVOT TOOLBAR

## LOAD & UNLOAD PROCEDURE

- Prepping

- Cap pivot bar spindle on topside of base. (Welder may put this cap on.)

- Put cover in open end of main beam and wire securely onto beam.

- Clip on the plate at the rear of the main beam.

- Bolt on the cover on the bottom of the spindle.

- Plug all of the misc. threaded holes and bolts located on the P.T.

### Loading Set Up

- Place three 1000 lb. spreader bars on the track, back to back, spaced two ft. apart.

- Hang the P.T. hanging device from the shackles of the first two 1000 lb. spreader bars.

- Hang two 30” x ¾” parallel hooks and a 10” x ¾” parallel hook off of the last 1000 lb. spreader bar.

##### Loading

- Attach the lifting shackle to the middle clevice on the bottom side of the P.T.

- Place a 6 ft. sling through the lifting shackle and attach both sling eyelets to the load block of the hoist and begin to lift.

Note:  Make sure hoist is centered directly above the P.T. to prevent any swinging once lifting has begun.

- Attach the clevice at the rear of the P.T. to the hanging device attached to the spreader bars.

- Attach the clevice on the main beam to the 30”/30”/10” hook combination.

- Make sure both clevices are attached securely and then start lowering the P.T. slowly.

- Remove the sling and the lifting shackle from the P.T.

- Once all the P.T.’s have been loaded, then bring the lifting shackle over to the unloaders.

##### Cover Plate Removal

- Blast operator is to remove the covers on both ends of the main beam and return them to the loading area for the P.T.

- Wash operator is to remove the spindle cover and blow any water or shot out of the cap and spindle.  Then put the spindle back on.

- Painters are to remove the bolt on plate on the bottom of the spindle and return it to the loading area for the P.T.

##### Unloading

- Attach the lifting shackle to the middle clevice on the bottom side of the P.T.

- Place a 6 ft. sling through the lifting shackle and attach both sling eyelets to the load block of the hoist and begin to lift.

Note:  Make sure hoist is centered directly above the P.T. to prevent any swinging once lifting has begun.

- Move the P.T. over to the assembly area and set it down.

- Remove the sling and lifting shackle.

- Remove the hanging device, the spreader bars and hooks from the track.

- Remove the plugs and the spindle cap from the P.T.

- Return the lifting shackle and the spindle cap back to P.T. loading area.

# Text boxes

Spindle cover

Bolt on cover plate on bottom of spindle

Clip on plate at rear of main beam

Cover for front of main beam

Lifting shackle

attached to clevice