PLATE SHEAR

SAFETY AND OPERATING PROCEDURE

A.	SAFETY

# Use proper lockout procedures when setting up the shear.  Shut off the power when leaving the machine unattended, and follow lock out procedures when doing total preventive maintenance.

# Your foot must be completely removed from the pedal box after completing each cut, on machines that are not equipped with light curtains or other safeguards.

# In a two-person operation, the helper must give the signal to cycle the shear. Always make sure you know the helper's position before cycling the machine.

# Always dispose of scrap material into the scrap metal bin to avoid injury on sharp corners.

# Don’t place any part of your body between the blades or between or under hold downs.

# Always put your tools back after you set up. Practice good housekeeping at all times.

- On shears equipped with a light curtain verify proper safety function.

- With the power on, with your hands a safe distance away from the shear blades.

- Cycle the shear.

- While the shear is in motion break the light beam (with a chip hook) to ensure the shear will shut off in mid stroke.

B.	QUALITY

# Check the stoppers frequently to maintain quality and eliminate mistakes.

C.	OPERATION

# Never cut material over 3/8" thick on the shear.

# Always ensure material is located under at least one hold down.

# Be sure when using bear paw magnet that you are not lifting more than one sheet at a time.

# Never feed material from the backside of the shear.

# Never attempt to shear a piece of material off that is shorter than three times it's thickness or machine damage will occur.

# Don't cut anything that has been heat-treated (example: torch cuts).

- When removing material with the forklift, avoid contacting the shear.

- Do not cut multi-stack parts.  One part or thickness of material is maximum.

- Do not leave the light curtain on “bypass” when you do not have full control of the machines foot pedal, hand controls, switches and levers.

# When working with short pieces where more length is past the blade than on the operator side, pieces must be back measured.