POWDER PAINT BOOTH

FAN MOTOR REMOVAL

- Follow Lockout Procedure and Lockout the booth.

- Remove the collector from the booth.

Note:  The booth must stay on line in order for there to be enough room so the forklift can get in to remove the fan motor.

- Pull all final filters around the motor cabinet off.

- Take the small trap door that is located above the motor sheave off.

- Have Electrical Maintenance unhook the cable and take off the connection box off the motor.

- Install a piece of ½” - ¾” x 10” x 10” board or hard rubber under the fan end of the motor, for support.

- Feed rope or sling down the small trap door and tie around the shaft under the sheave to help lower the motor.

- Bring a forklift with the fork touching one another into the final filter opening right behind the motor.  Use the opening that is the second one in from the north side of the collector.

- Loosen the motor and take the belts off.

- Remove all nuts that are holding the motor and lie the motor down onto the forks of the forklift.  Tie or sling the motor to the forks and back out and bring down.

Note:  When backing out take extra caution that the forks or the fan motor does not damage the final filter opening.

- To install the motor reverse the procedure.