# SAFETY LIMITS - WEIGHT AND SIZE

POWDER LINE

A.  TRACK WEIGHT LIMITS

Figure 1                                                              Graph 521

1.	Maximum weight is 500 lb. per carrier roller.

a).  use load bars if weights are larger than

500 lb. per carrier.

b).  maximum 1,000 lb. per load bar.

2. 	Overall track loading to be less than 100 lb./ft.

B.  SIZE LIMITS

- Parts must be within the following limits.

a).  Maximum width is 24 inches from center of track to either side of part.

b).  Maximum height. Is 30 inches below top of (-beam.

c).  Minimum height. Is 11 feet below top of  (-beam.

2.	Guidelines for long items.

a).  Maximum length is 35 feet.

- item must be spaced equally beyond support points.

b).  Load long items on 8 foot centers if possible.

c).  Distance between supporting points must not exceed 12 feet.

LIQUID LINE

- TRACK WEIGHT LIMITS

- Maximum weight is 100 lb.  per carrier roller

- Overall track weight limit is 50 lb./ft.

- SIZE LIMIT

- Vertical

a).  Minimum of 2 feet from top of parts to the top of the 4 inch (-beam

b).  Maximum of 5 feet from the bottom of the part to the top of the 4 inch (-beam.

- Horizontal

a).  Maximum length of the parts is 3 feet, with a maximum of 6 inches before the front hanger and 6 inches after the rear hanger.

b).  Maximum width of the parts is 2 feet and centered on the line, (1 foot on each side of center).

c).  When parts are hung with the maximum length and height, a space of one (1) trolley

must be left between loads so that the loads do not bind at the corners.

| SEPT HOOK LOAD RATING CHART |
| --- |
| HOOK DIA. | APPROX. |  | LOAD RATING |
| IN INCHES | HOOK LENGTH | DESCRIPTION |  |
| ¼” | 4" | ROUND BAR | 50 LBS |
| ¼” | 8" | ROUND BAR | 50 LBS |
| 3/8” | 11" | ROUND BAR | 150 LBS |
| 3/8" | 11" | ROUND BAR OFFSET 90 DEG | 150 LBS |
| 3/8" | 13" | ROUND BAR DOUBLE HOOK | 200 LBS |
| 3/8" | 18" | ROUND BAR | 200 LBS |
| 3/8" | 40" | ROUND BAR | 200 LBS |
| 3/8" | 8" | SQUARE BAR | 250 LBS |
| 3/8" | 8" | SQUARE BAR OFFSET 90 DEG. | 250 LBS |
| 3/8” | 16" | SQUARE BAR | 200 LBS |
| ½” | 7 1/2" | ROUND 90 DEG | 300 LBS |
|  |  | OFFSET SMALL ANGLE |  |
| ½” | 7 1/2" | ROUND 90 DEG OFFSET LARGE ANGLE. | 200 LBS |
| ½” | 8" | ROUND BAR | 300 LBS |
| ½” | 16 3/4" | ROUND BAR | 300 LBS |
| ½” | 33" | ROUND BAR | 350 LBS |
| ½” | 8" | SQUARE BAR | 350 LBS |
| ½” | 8" | SQUARE BAR OFFSET 90 DEG. | 350 LBS |
| ½” | 16" | SQUARE BAR | 450 LBS |
| ½” | 32" | SQUARE BAR | 300 LBS |
| 5/8” | 8" | ROUND BAR | 550 LBS |
| 5/8” | 8" | ROUND BAR OFFSET 90 DEG. | 600 LBS |
| 5/8" | 18" | ROUND BAR | 500 LBS |
| 5/8" | 18" | ROUND BAR OFFSET 90 DEG. | 500 LBS |
| 5/8" | 30" | ROUND BAR | 550 LBS |
| ¾” | 18" | ROUND BAR | 950 LBS |
| ¾” | 30" | ROUND BAR | 1000 LBS |
| 5/16” | CHAIN | BOOM HANGERS SMALL | 1000 LBS |
| 5/16” | CHAIN | BOOM HANGERS LARGE | 1000LBS |

Note:

- Paint line hooks are only meant to support items on the paint track and must never be

used as rigging for lifting and moving items  with an overhead hoist.

- The weight that each hook supports from the paint line must never exceed the load

rating of that hook.

RACKS

| Rack Number | Rack Description | Load Rate Per Hook | Load Rate Per Rack |
| --- | --- | --- | --- |
| R1 | Shank Rack Light Straight 1/4" dia. Hook | 75 lbs | 700 lbs |
| R2 | Shank Rack Light Sideways 1/4" dia. Hook | 75 lbs | 700 lbs |
| R3 | Shank Rack Heavy Straight 3/8" dia. Hook | 139 lbs | 700 lbs |
| R4 | Shank Rack Heavy Sideways 3/8" dia. Hook | 139 lbs | 700 lbs |
| R8 | "82" Rack with 3/8" dia. Pegs | N/A | 378 lbs |
| R9 | "95" Rack with 1" dia. Pegs | N/A | 600 lbs |
| R10 | Universal Rack | N/A | 616 lbs |

Note:  the weight of the items which are loaded on racks must never exceed:

a)  the load rating of the rack’s hooks;

b)  the load rating of the rack itself.