SMALL PIPEBENDER

A.	SAFETY

- Do not attempt to bend the material while holding on to the material.  Your fingers can easily be pinched or your clothing can snag, pulling you into the machine.

- Never stand in the Bend Zone.  Long pieces make a sweeping motion.

- Make sure that the Bend Zone is clear.

B.	OPERATING

- Make sure all tooling is properly selected, mounted and aligned.

- Make sure your work piece fits into the tooling properly when being bent. Be cautious of clearance, either excessive or insufficient which will effect the quality and efficiency of the operation.

- Make sure work piece does not catch on the side of the machine when being bent.

- Always put your tools back after you set up.  Practice good housekeeping at all times.

- Report anything out of the ordinary to your Supervisor.

C.	CHECKS

- Make sure parts are checked periodically on the parts jig, or manually, after being bent.

- Periodically inspect the condition of your tooling, inspect for wear, cracks, galling, (built up of material on the clamps/die), burrs, etc.