HEAVY HARROWS LOADING

PROCEDURE

Warning:  Due to the size of the Heavy Harrow it is essential that the harrow is loaded exactly as per the following outline. Failure to follow these procedures will result in damage to the building, equipment, and or personnel.

- Ensure that the following are set up for using a shank rack and are loaded after the last heavy harrow.

i     AW-116W 	1 per assembly

ii.	AW-117W 	1 per assembly

iii.	AW-118W 	1 per assembly

One heavy harrow uses 2 heavy harrow hooks (25 3/4" x 3/4" with a 3" hook seat width).

2.	Load harrow

a.	Using the heavy harrow lifting chains inserted in the middle harrow bar lift the harrow.

b.	Load all harrows so they are facing outside of track, and with the control arm at the bottom.

c.	Hang the harrow from the front (1st tube) harrow tube with the hooks on the outside of the main harrow frame but as close as possible to the frame.

3.	Secure the tine adjustment control arm.

a.	Move the control arm into a 90 angle with the heavy harrow. This will align the control arm to the middle adjustment hole.

b.	Insert a wire tie through the middle adjustment hole and twist it tight. This is done twice with two wire ties. This will keep the control arm from dropping and snagging on the paint line.

4.	Inspect the harrow for the following: Assembly is responsible to do it - the Company must ensure that it is done properly):

a.	Ensure tine adjustor arms are secured (will not rotate) by the securing rod (harrow tie) that is inserted in the adjustor arm holes on the following tubes:

iv.	Front tube & second tube

v.	Third tube & fourth tube.

Note:	The one end of the harrow ties must have a cotter pin inserted to ensure that the tie will stay in place.

b.	Ensure that the 5th harrow tube is secure and will not rotate. The 5/8" bolt should ensure this.

c.	Ensure harrow tines are tie wired in the following pattern.

i.	Harrow tube tines front, 2nd, 3rd, and 4th all point to the back of the harrow (down).

ii.	Harrow tube tines #5 all point toward the front (up).