PRESSURE WASHER

OPERATING PROCEDURE

Warning:  Do not allow the washer pump to run more than 2 minutes when not in use.  The pump will overheat resulting in damage.  The couplers are rated for a maximum of 2000 psi.  Do not operate the pump above 2000 psi.

- Locate the water tap to the left of the titration table and turn it off.  Disconnect the hose which is feeding fresh water to the stage 4 riser and connect the water hose from the pressure washer.  Ensure the connection is secure and turn the tap on.

- Locate the 600 volt power outlet to the left of the titration table and connect the 600v power cable from the pressure washer to this outlet.

- The pressure washer is on castors and can be moved to any location along the wash where work is being performed.

- Turn the pressure washer on.  The switch is located on the side of the frame.

- Perform required work.

- Turn pressure washer off. Turn washer tap off and pull the trigger on the wand to release the pressure from the water hoses.

- Disconnect the water hose and the 600V cable from the outlets on the side of the wash.

- Roll up hoses and cable and return everything to its storage location.

- Re-connect the fresh water riser water hose to the water outlet beside titration table.

Note:  Report any unusual noises or malfunctions to Maintenance immediately.